## Slide 1
REMOTE SENSING METHODS FOR INVESTIGATING OUTGOING INFRARED RADIATION OF RECENT LARGE REGIONAL FAULTS AND ITS TERRESTRIAL HEAT FLOW AND GEOCHEMICAL HALOES
N.V.Vilor, L. D.Andru-laitis, O. V.Zarubina, B. S.Danilov, and A. V.Klyuchevsky
Institute of Geochemistry SB RAS, Irkutsk, Institute of the Earth’s Crust SB RAS, Irkutsk , Russia
THE MOUNTAIN KING’S ARMCHAIR

## Slide 2
Purpose
Determination of intensity of outgoing IR radiation flow of large seismoactive regional faults, which are expose by surface heat flows by remote sensing method and correlation this flow with transfer of mobile chemical elements and its geochemical flows
Items
the remote sensing method of mapping of distribution of intensity of outgoing IR radiation flow for different geodynamic situation
the investigation of nature of surface outgoing IR radiation flow
the investigation of distribution of mobile chemical elements into surface formations of regional faults
the calculation of its geochemical flows by using the conception of geochemical barriers

## Slide 3
The subsurface heat flow from the upper part of the earth’s crust.
The flow was formed inside the radiating layer of the ground
F = Fgr + Fc + F phc + Fd
The outgoing electro-magnetic
radiation in IR heat band
satellites NOAA, TERRA, AQUA
The area of subsurface heat-mass transfer
via heat-carriers
Fd
F
L
The area of computing the geometric factor
F–surface heat flow (mW/m2)–the effective surface radiation of the geostructure
THE SCHEME OF THE ORIGIN OF THE SURFACE INFRARED
RADIATION OF THE LARGE REGIONAL FAULTS
Brightness of the outgoing electro-magnetic radiation
in the IR band mea-sured by satellites

## Slide 4
Type of regional deformation | Region
Tention, rifting | Baikal rift zont (BRZ), Rhine graben, “Afar triangle” + Eastern – African rift
Displacement | San – Andreas transform fault system
Collision | Himalayas, Western- Copetdag structural arc
Block compression, ramp situation | Tarim basin and its folded frame
Geodynamical situations of manifestation of outgoing surface IR radiation flow of large seismoactive regional fault

## Slide 5
Distribution of outgoing surface IR radiation in the BRZ. 1 – 5 the largest rft depressions: 1- Baikal, 2- Hovsgol, 3 - Tunka, 4 – Barguzin, 5 – Upper Angara, 6 - Darkhat
Rift situation. Outgoing surface IR flow large tectonic depressions BRZ. A. Tunka depression. B. Bargoozin depression
A
B

## Slide 6
Upper Angara
Tunka
Bargoozin
The temporal maps of regional permeability along large faults BRZ for 1976 – 1994 years
A
B
C
The low length wave of geometric component of plots of outgoing surface IR flows of BRZ’largest faults

## Slide 7
Мангейм
Страсбург
The structural map of Rhine graben. thermal water springs (after Friedrichsen,1981
Outgoing surface IR flows map of Western Europa part with Rhine graben. A, B, C – large regional faults (after Gorni V.I. 2007)
famous water spring
А
C
B
Fraidurg
Strasburg
Frankfurt

## Slide 8
B
The outgoing surface IR flow map of Afar depression and mouth of Eastern African rift
The structural map of Afar
The correlation of the depth of bedding of Moho surface and outgoing IR flow
The depth of bedding of Moho surface, km
The
IR
flow

## Slide 9
B
A
C
The displacement geodynamic situation. IR radiation distribution on western part of USA(A) and structural maps of San-Andreas transform fault (B) and Big Basin province (C) (after R.L.Cook andJ.A.Thomson, 1970)

## Slide 10
F
F
F
F
F
F
1
2
3
4
5
6
IR radiation anomalies of the surface of large faults of San Andreas system (1-3) and on faults of Big Basin province (4-6) F –fault’s tracks
Points of dimention
IR
radia-tion temperatu-re, K

## Slide 11
Caspian Sea
Kara-Kum desert
Kura-Bugaz gulf
South-Turkmen fault
Aladag-Binalud displacement
Structural (A) and IR radiation flow intensity (B) maps of the main bord er
fault of Himalayas (after Ganser A.1967, Tronin,Saraf, 2010)
A
B
Collision situation. Structural (C) and IR radiation flow intensity (D) maps of Copetdag structural arc (after Tronin, 2010)
South-Turkmen main fault
C
D

## Slide 12
These boundaries are located on the slopes of the uplifted block of the upper crust, which corres-ponds to the massif of the Tarim platform.
The new map of Moho surface for Chinese territory
by Baranov, @Earth Physics, N1, 2009
The Tarim
platform
Ramp situation

## Slide 13
Brightness of the contrast outgoing surface IR flow for the Tarim platform and its framing (January 2001, night)
The distribution of IR flux intensity across Tarim platform
IR flux
IR flux
The northen boundery
The border zone
desert
range
Faults
The southern boundary
desert
Border zone
range
faults
Basin’s upluft
The distance, km

## Slide 14
Kalpin-tag structure
Kuruk-tag structure
months
IR flow
The derivative of IR flow
The minimum of derivative
The calcula-tion of quasista-tionary IR flow
Mazartag structure

## Slide 15
The transition to the values of brigthness measured for the surface IR flow can be made with the use of the following relation
F = L · G (Gossorg, 1980) (1),
were F - surface IR flow , L - brightness IR flow, G - geometric factor, which writes
G = π ·S · sin2 α = 6.8704 (m2. ster).
Hence the surface IR flow F computed by (1) makes: F = 6.8704 L (mW).
Values of F are added for the components, which form its balance. The addends of such a balance include: Fgr – heat flow of the active ground layer (the result of heat inertia), Fc – heat effect of the surface condensation or crystallization of water vapor, F pch – heat effect of the process of oxidation of gases coming from the ground in the upper part of the active layer, Fd – component of the deep heat flow. Hence, we have:
F = Fgr + Fc + F pch + Fd
The sub-surface endogenic flow Fd is the sum of influences of the conductive and the convective components upon the radiating layer. The difference between the value of the near-surface endogenic flow Fd and the near-surface conductive component Fcnd computed represents the share of the convective component Fcnv . Fcnv = Fd – Fcnd
Fault | Bright-ness flow, L мW/м2.сr.μμм | Surface heat flow, F мW | Depth part of F, F dep, мW | Portion of F depth, мW |  | The part of kon-vektive portion, %
 |  |  |  | konduc-tive F conda | konvec-tive Fconve | 
Tunka | 103.027 | 707.84 | 323.37 | 25.46±4.14 | 297.86±4.18 | 92
Bargoozun | 85.466 | 587.19 | 362.14 | 25.44±2.69 | 336.71±2.7 | 93
Near-sea | 112.242 | 771.15 | 339.36 | 20.94±1.67 | 318.42±1.67 | 94
Border zone of platf. | 103.64 | 708.09 | 289.62 | 18.79±0.8 | 270.86±0.77 | 94
The calculated surface heat flow of large regional faults of BRZ
Fault structu- re | Surface heat flow F, mW | Depth conduc-tive part of F, calulated | Portion of Fdepth, mW | 
 |  |  | konducti-ve, F conda | konvek- tive, F conve
Mazartag | 61.47 | 40 | 19.59 | 41..88 (68)
Kalpintag | 196.56 | 40 | 19.59 | 176..97 (90)
Choltag | 199.87 | 44 | 20.22 | 179..65 (90)
Kuruktag | 186.86 | 45 | 20.38 | 166.48 (89.1)
Altuntag | 256.56 | 43 | 20.06 | 236.48 (92)
The calculated surface heat flow of large regional faults of Tarim basin and it folded frame

## Slide 16
The set of geochemical samples on large seismoactive regional fault’s trakcs of BRZ
A. Border regional zone of Siberian platform and Tunka fault, B. Bargoozin depration
A
B
Plots of volatile chemical ore element’s concentration distribution into surface formations of Bargoozine regional fault
The concentration is g / t
Depth, cm

## Slide 17
Fault | n | Cm | B | Cu | Zn | Pb | As | Ge | Mo | Sn | Ag | Tl | Hg | Со | Сr | Ni | V
Tunka | 88 | Х | 42. | 34.2 | 75.40 | 13.9 | 11.6 | 1.2 | 1.98 | 2.6 | 0.2 | 0.9 | 0.1 | 16.1 | 81 | 68 | 68.2
 |  | ±σ | 2.0 | 1.32 | 1.12 | 1.31 | 1.62 | 0.4 | 1.35 | 0.9 | 0.2 | 1.0 | 0.1 | 1.3 | 1 | 1 | 1.3
Bargoo-zin | 75 | Х с | 14.3 | 25.9 | 112.1 | 17.9 | 6.14 | 1.2 | 1.55 | 3.1 | 0.2 | 0.7 | 0.1 | 16.7 | 51 | 39 | 95
 |  | ±σ | 1.1 | 1.18 | 1.05 | 1.03 | 1.33 | 0.3 | 1.25 | 1.0 | 0.1 | 0.4 | 0.1 | 1.0 | 1 | 1 | 1
Border zone of platform | 91 | Х | 20.6 | 22.8 | 69.65 | 12.4 | 17.4 | 1.2 | 1.25 | 2.3 | 0.3 | 0.8 | 0.6 | не определены |  |  | 
 |  | ±σ | 2.1 | 1.28 | 1.25 | 1.59 | 2.21 | 0.6 | 1.82 | 1.2 | 0.3 | 1.4 | 1.5 |  |  |  | 
Geotherm. field Kucheger |  | Х | 20.3 | 23.9 | 88.65 | 18.2 | 14.3 | 3.9 | 1.14 | 2.2 | 0.74 | 0.6 | 0.1 | 11.9 | 42 | 36 | 60.3
 |  | ±σ | 1.1 | 1.33 | 1.19 | 1.1 | 1.61 | 1.7 | 1.09 | 1.1 | 1.5 | 0.4 | 0.2 | 1.1 | 1.1 | 1.2 | 1.1
Fault | Indicators of geochemical specialization of faults |  |  |  |  |  | 
 | High concentration, g / t |  | According to dispersion |  | According to geochemical association |  | 
 | Cmax | Back-ground | 9 elements F1/F2 | 15 elements, F1/F2 | 9 elements | 15 elements | Main / secondary
Tunka | B, Cu, Cr | B, Cu | Ge, B / Tl, Mo | B / Mo | Tl, Ag, Mo, B | Hg, As, Ag, Mo | Ag, Mo/ Hg, As, Tl
Bargoozin | Zn, V | Zn, V | Ag, Cu / Pb, Tl | Ni, As / Pb, Mo | Tl, Cu, Ag, | Mo, As, Tl | Tl / Cu, Ag, As
Border zone of platform | As, Hg | Hg | Cu, Zn / Tl, Mo | Mo, As / Zn | Mo, Tl, Ag | Mo, Hg, As, Ag | Mo, Ag / Tl, Hg, As,
Geothermal field Kucheger | Ge, Ag | Ge, Ag | не расс- читано | Zn, Pb / V, Co | не рассчит. | Hg, Ag, Mo, Ge | Hg, Ag, Ge / Mo
Geochemical indicators, associated with surface outgoing IR flow of large seismoactive faults of BRZ

## Slide 18
П, geochim. flow = [С comp : (S ∙ t)] ∙10 6 = kg/km2 ∙ year.
Fault | geochim. flows, kg/km2 ∙ year |  |  |  |  |  | SHF, мWт | F dep, мWт
 | As | Tl | Hg | Ag | Mo | Ge |  | 
Tunka | 3.252 | 0.226 | 0.020 | 0.089 | 0.189 | не оп | 707.84 | 323.37
Bargoo-zin | 0.879 | 0.139 | 0.013 | не оп | не оп | не оп | 587.19 | 362.14
Border zone | 1.671 | 0.229 | 0.037 0.055 | 0.018 | 0.139 | не оп | 708.09 | 289.62
Thermal zone Ku-cheger | 21.44 | 0.413 | 0.021 | 0.479 | не опр | 7.267 | 74 Wт/м2 | 9.553 МW
Surface ionization level of near ground air for Tunka fault track
fault
rim zone
depression
Cordomorphous cloud above Tunka fault track
fault track
Geochemical flows of large seismoactive regional faults of BRZ

## Slide 19
Thank's a lot for Your attention
Ionospheric perturbations above large seismoactive fault, associated with Wenchuan Mw=8.0 earthquake on 12 May 2008 in Sichuan, China (after Xiao-Li Ding et al., Urumqi, 2009)