## Slide 1
Numerical investigation of the interaction between hydraulic fractures and natural fractures in porous media based on an enriched FEM
Yun Zhou1, Diansen Yang1, Xi Zhang1,2, Weizhong Chen1
1State Key Laboratory of Geomechanics and Geotechnical Engineering
Institute of Rock and Soil Mechanics of Wuhan, CAS
2On leave from CSIRO Energy, Melbourne, Australia
July 2019 Novosibirsk

## Slide 2
Institute of Rock and Soil Mechanics, Chinese Academic Science founded in 1958 at Wuhan, Hubei Province
433 staff (Prof.Ge Xiurun, Academician); 251 scientists; 230 postgraduate students
State key laboratory of Geomechanics and Geotechnical engineering
Research funds: ~ 150 millions RMB/ year;
Scientific Outcomes: >300 SCI publications/year, 50 patents/ year

## Slide 3
Introduction
Numerical Model
Validation
Numerical Results
Conclusions
Outline

## Slide 4
Applications Of Hydraulic Fracturing
Petroleum
Crossing
Arrest
Offset
Different interaction scenarios
What is the interaction mechanisms between HFs and NFs and how to quantify？
NFs
Mining

## Slide 5
Physical process of hydraulic fracturing (Kovalyshen and Detournay, 2010)
Fluid flow within fracture
Fluid leakage through the surface
Pore fluid flow in matrix
Crack tip propagation
Deformation of the matrix
(Llanos 2017 RMRE)
Rock are not always impermeable
Fluid leakage is severe during the crossing process
The poroelasticity of the matrix
The influence of fluid leakage on interaction scenario
Hydraulic Fracture Growth in Porous Media

## Slide 6
2D XFEM Method
FEM
XFEM
Fully coupled model based on XEFM (Lecampion 2009)
Interaction mechanisms between HFs and NFs (Gordeliy and Peirce, 2013)
Consider 2D fluid leakage during fracture crossing (Khoei and co-authors…)
Multiple fractures include intersection (Dahi and Olson, 2013,…)
XFEM for Hydraulic Fracturing
Difficulties in mesh generation
Refined mesh near crack tip
Re-meshing after crack propagation
High computational efficiency

## Slide 7
Introduction
Numerical Model
Validation
Numerical Results
Conclusions
Outline

## Slide 8
Governing Equations
Computational Domain
Fluid leakage from the surface
Fluid pressure applied on opened fracture surface (No lag)
Frictional contact of NF
An initial opening is assigned to NFs
Governing equations
①Equilibrium equation
②Continuity equation in matrix
③Continuity equation in fracture

## Slide 9
Weak form of governing equations
Fluid Leakage from surface in 2D
(2014 Khoei)
is assumed for pressure field
Internal boundary conditions
2D Model

## Slide 10
XFEM Discretization
Enrichment strategy for single fracture
U
P
Shape Functions
Signed distance function

## Slide 11
XFEM Discretization (Extended to X-intersections)
Heaviside enriched node
Junction enriched for U(left junction)
Junction enriched for U(right junction)
U
P
Junction enriched for P(left junction)
Junction enriched for P(right junction)
m, s are fracture numbers.
Fracture Intersections
Left
Right
Left
Right
Left
Right
Khoei et al, 2018 for junctions

## Slide 12
Natural Fracture Friction Law
Penalty Method
Substitute it as a traction in weak form and integration
Subregions and integral scheme
1. Normal XFEM element
2. T-junction element
3. Intersection element

## Slide 13
HF coalescence
The maximum hoop tensile stress criterion is adopted when dc>rs
HF merge with the NF when dc<rs
HF re-initiation
Calculate the NF-parallel normal stress along the right side of NF
Determine the average tensile stress of each fracture segment(1,2,3…)
The HF will cross if average tensile stress is higher than the tensile strength
New HF propagates perpendicular to the direction of maximum principle stress
HF-NF Intersection
After find fracture propagation direction (Erdogan and Sih, 1963)

## Slide 14
Solution procedure
U-P Discretized equation
Time domain discretization
Residuals of coupled equations
N-R Iteration step
Jacobian matrix
Numerical Equations

## Slide 15
Introduction
Numerical Model
Validation
Numerical Results
Conclusions
Outline

## Slide 16
Single Fracture
Hydraulic fracturing in permeable media—Solve 2D leakoff problems
Computation Model
 | Fluid viscosity μ | Injection Rate Q0 | Critical stress intensify factor KIC | Matrix permeability Km | Dimensionless toughness κ
Case 1 | 0.01Pa·s | 0.001m2/s | 1.8MPam0.5 | 1×10-14m2 | 0.99
Case 2 | 1×10-4Pa·s | 0.0005m2/s | 2.2MPam0.5 | 1×10-15m2 | 4.37
Parameters | Value
Elastic modulus E | 16GPa
Poisson ratio v | 0.2
Biot’s coefficient α | 1
Porosity ϕ | 0.2
Solid density ρs | 2000kg/m3
Fluid density ρw | 1000kg/m3
Solid compressibility Ks | 36GPa
Fluid compressibility Kw | 3GPa
Input Parameters
Material Parameters

## Slide 17
Dimensionless leak-off coefficient
C1=0.17（T=10s）
C2=0.13（T=10s）
Numerical results vs KGD Solution (Hu and Garagash, 2010)
Validation

## Slide 18
Introduction
Numerical Model
Validation
Numerical Results
Conclusions
Outline

## Slide 19
HF-NF Interaction
Computational model (2D)
Case | NF coefficient of friction λ | NF initial opening w0 | Injection rate Q0 | Fluid viscosity μ | Matrix permeability Km
A | 0.4-1 | 0.025mm | 6×10-4m2/s | 10mPas | 1×10-14m2
B | 0.8 | 0.01mm-0.075mm | 6×10-4m2/s | 10mPas | 1×10-14m2
C | 0.8 | 0.025mm | (4-10)×10-4m2/s | 10mPas | 1×10-14m2
D | 0.8 | 0.025mm | 6×10-4m2/s | (5-100)mPas | 1×10-14m2
E | 0.8 | 0.025mm | 6×10-4m2/s | 10mPas | (0.1-2)×10-14m2
Parameters | Value
Approaching angle(αc) | 90°（A-E）
Horizontal confining stress (σx) | 5MPa
Vertical confining stress (σy) | 4MPa
Critical stress intensify factor (KIC) | 1.5MPam1/2
Distance between Point E and F (Ld) | 1m（A-E）
Fracture deflection Cases

## Slide 20
NF coefficient of friction λ
T=2s
Smaller coefficient of friction λ
Larger injection pressure peak
Slippage of NF becomes easier
More fluid is stored in HF
Crossing becomes difficult
F

## Slide 21
T=2s
T=2s
Smaller initial opening w0
Larger injection pressure peak
Less fluid can flow in NF
Smaller fluid pressurized zone
Larger probability for crossing
NF initial opening w0

## Slide 22
Lower injection rate(Same volume Q0T=C)
Larger injection pressure peak
More leakage and less fluid stored in NF
Smaller opening of NF
Larger probability for crossing
Q · T=2E-3
Q · T=2E-3
Injection rate Q0

## Slide 23
Injection rate Q0 (contd.)

## Slide 24
T=2s
T=2s
Lower fluid viscosity μ
Pressure peak decreases and re-increases
HF meets NF at early time
More leakage and smaller opening of NF
Smaller probability for crossing
Fluid viscosity μ

## Slide 25
T=2s
Larger matrix permeability
Larger injection pressure peak
Less fluid can flow into NF
More leakage and smaller opening of NF
Larger probability for crossing
Matrix Permeability Km

## Slide 26
Normal opening of HF and NF at different times
Crossing(90°)
Offset(75°)
Diversion(60°)
Diversion(45°)
Pressure contours（Pa）at T=12s
Fracture Crossing Cases
Different Approaching angles αc

## Slide 27
Introduction
Numerical Model
Validation
Numerical Results
Conclusions
Outline

## Slide 28
A fully coupled hydro-mechanical model based on X-FEM is developed.
Treatment for fracture intersection in X-FEM is considered.
Injection pressure changes are different than impermeable matrix
Strong leakage when lower injection rate and fluid viscosity are used
Different interaction scenarios between HF and NF can be handled by the proposed model.
Conclusions
Future work
More comparisons
More cross criteria between HF and NF need to be tested
Fracture network formation modeling

## Slide 29
Thank you for your attention！
Email: zhouyun17@mails.ucas.edu.cn
or
xi.zhang@csiro.au